## Slide 1
Community Energy
In a Zero Carbon Housing Project
11th September 2020

## Slide 2
Topics
How does community energy work
What do we mean by zero carbon homes?
Energy supply options
Implications of different design decisions on different organisations
Legal constraints around selling energy
Ownership of equipment & market issues
Long term management issues

## Slide 3
How Community Energy Works

## Slide 4
Burneside’s Complexities

## Slide 5
Zero Carbon Homes
Calculating carbon: impact of grid decarbonisation
Building efficiency standards:
  Building Regulations – regulated & unregulated emissions
  Passivhaus
  AECB
Fabric efficiency vs zero carbon supply: who pays?
Design vs in-use energy demand
Embedded carbon in construction

## Slide 6
Zero Carbon Energy Supply
Net zero supply
  Local renewable energy generation kWh = Local demand kWh
  Peak generation exported, peak demand imported
Islanded supply
  All demand is supplied from local generation
  Ability to be completely separate from grid
  Reliant on storage and demand management

## Slide 7
Energy Supply Options
Transport
  Electricity for EV charging
  Local or centralized storage? Vehicle to grid?
Heat
  Space heating: heat pumps (individual or central), MVHR, direct electric
  Water heating: heat pumps, solar thermal, direct electric
  Distribution: individual systems, shared ground loop, district heating
  Storage: DHW tanks, inter-seasonal?
Electricity
  PV only realistic option – daily/annual supply/demand profile problems
  Import from Croppers – not zero carbon

## Slide 8
PV Supply/Demand Profile

## Slide 9
Electricity Demand
Scenario | Average New House | AECB Silver + std power | Passivhaus | Passivhaus + low power | Passivhaus + low power +high EV
Number of homes | 70 | 70 | 70 | 70 | 70
Assumed Ave Demand per house | kWh | kWh | kWh | kWh | kWh
Heat | 6500 | 4500 | 2000 | 2000 | 2000
Electric Power exc heat and EVs | 3200 | 3000 | 2000 | 1500 | 1500
EV charging | 750 | 750 | 750 | 750 | 1500
PV capacity needed kW | 575 | 500 | 335 | 285 | 360
PV potential on roofs @ 3kW per roof | 210 | 210 | 210 | 210 | 210
Ground mounted PV needed kW | 365 | 290 | 125 | 75 | 150

## Slide 10
Legal constraints on selling energy
Micro-grid required for direct electricity sales to domestic customers
  Greater income from sales
Alternative: buying scheme for householders
  Complex and limited value
Net zero supply via National Grid
  Unlikely to justify investment
Highly regulated sector: requirement to allow customers to change supplier
Heat less regulated but easier to get it wrong: Code of Practice for heat networks
Market implications?

## Slide 11
Design Decisions impacting BCE
Housing numbers => system size & financial viability
Fabric efficiency /solar gain => system size, costs for occupants
Housing size/type => direct impact on demand
Layout => density affects costs for microgrid / heat network
Orientation/ roof design/shading => options for PV locations
Location => connectivity of energy systems
Transport => accessibility affects EV demand
Tenure => lease/ownership of equipment, management plan
Construction decisions: who owns risk if not built to specification?

## Slide 12
Ownership & financial contributions
Owned by home owner? Paid for by developer?
  Individual heat pumps/heat exchangers? PV on roofs? Individual batteries?
Owned by ESCo?
  Centralised heat supply system? Shared ground loops? External PV? External batteries? PV on leased roofs?
Grid supply costs
  Constrained site – additional costs for developer?
  Benefits of local supply? Who gains?
Implications for mortgages and insurance
What about any social housing?
Market implications?

## Slide 13
Operational Risk
Long term management by ESCo
Design & build decisions affect operating costs
  How much can be passed on to householders?
  What if not financially viable?
Reputational risk for all involved… but likely to stay with BCE for the longest